## Slide 1
Data Communication Concepts
Static and Dynamic IP Addressing

## Slide 2
Overview
Static IP Address Assignment
Dynamic (Automatic) IP Address Assignment
Static (Manual) versus Dynamic (Automatic) IP Configuration
DHCP (Dynamic Host Configuration Protocol) Service
Simulation in Packet tracer
Outline
Outline

## Slide 3
In this lab, we will learn about static and dynamic IP addressing.
Outline
Overview

## Slide 4
By default, client computers obtain TCP/IP configuration information automatically from the Dynamic Host Configuration Protocol (DHCP) Service. However, even in a DHCP-enabled environment, you should assign a static IP address to selected network computers.
For example, a computer running the DHCP service cannot be a DHCP client, so it must have a static IP address.
If the DHCP Service is not available, you must also configure the computer to use a static IP address. For each network adapter card that uses TCP/IP in a computer, you can configure an IP address, subnet mask, and default gateway.
Outline
Static IP Address Assignment

## Slide 5
If a server running the DHCP Service is available on the network, it can automatically assign the configuration information to the DHCP client.
Using DHCP to configure TCP/IP automatically on client computers can simplify administration and ensure correct configuration information.
To use the DHCP service to provide clients with the configuration information automatically, however, you must first configure a computer as a DHCP client.
To configure a DHCP client, open the TCP/IP properties dialog box and click obtain an IP address automatically (by DHCP).
Outline
Dynamic (Automatic) IP Address Assignment

## Slide 6
NOTE: In a small private network where a DHCP server is not available, you can use the Windows 2000 Server feature called Automatic Private IP Addressing (APIPA) to automatically assign IP addresses for you.
The Internet Assigned Numbers Authority (IANA) has reserved 169.254.0.0 through 169.254.255.255 for Automatic Private IP Addressing.
Outline
Dynamic (Automatic) IP Address Assignment (Continue…)

## Slide 7
Outline
Static (Manual) versus Dynamic (Automatic) IP Configuration
Configuring TCP/IP manually | Configuring TCP/IP using DHCP
Users can pick an IP address at random rather than obtaining a valid IP address from the network administrator. | Users no longer need to acquire IP addressing information from an administrator to configure TCP/IP.
Typing in the IP address, subnet mask, or default gateway can lead to problems ranging from difficulty communicating, if the default gateway or subnet mask is incorrect, to problems associated with a duplicate IP address. | Valid IP addressing information ensures correct configuration, which eliminates most difficult-to-trace network problems.
There is administrative overhead for networks if you frequently move computers from one subnet to another. | Having servers running the DHCP Service on each subnet eliminates the overhead associated with having to manually reconfigure IP addresses, subnet masks, and default gateways when you move computers from one subnet to another.

## Slide 8
DHCP is a TCP/IP standard for simplifying the management of IP configuration.
Each time a DHCP client starts, it requests IP addressing information from a DHCP server. This addressing information includes the following:
  An IP address
  A subnet mask
  Optional values, such as a default gateway address and a DNS server address.
Outline
DHCP (Dynamic Host Configuration Protocol) Service

## Slide 9
When a DHCP server receives a request for an IP address, it selects IP addressing information from a pool of addresses defined in its database and offers the IP addressing information to the DHCP client.
If the client accepts the offer, the DHCP server leases the IP addressing information to the client for a specified period.
Outline
DHCP (Dynamic Host Configuration Protocol) Service

## Slide 10
The DHCP Lease Process
DHCP uses a four-phase process to lease IP addressing information to a DHCP client for a specific period: DHCPDISCOVER, DHCPOFFER, DHCPREQUEST, and DHCPACK.
Outline
DHCP (Dynamic Host Configuration Protocol) Service

## Slide 11
for the following network assign a TCP/IP configuration information for each needed device in packet tracer;
1. Using static IP addressing assignment
2. Using dynamic IP assignment, DHCP server is not available.
3. Using dynamic IP assignment with existence of DHCP server.
Outline
Simulation of DHCP in Packet Tracer

## Slide 12
THANK YOU