## Slide 1
Data Communication Concepts
Troubleshooting IPv4 Network Connectivity
Lab Four

## Slide 2
Overview
Ipconfig Command
Ping Command
Trace Route Command
Outline
Outline

## Slide 3
In this lab, we will learn about troubleshooting and testing command .
Outline
Overview

## Slide 4
You can use the ipconfig utility to verify the TCP/IP configuration parameters on a host. This helps to determine whether the configuration is initialized or whether a duplicate IP address exists. To use this tool enter to the command window (cmd) in each host and write the following syntax:
ipconfig
Outline
Ipconfig Command

## Slide 5
Outline
Ipconfig Command
1
2

## Slide 6
Outline
Ipconfig Command
3

## Slide 7
Outline
Ping Command
PING, the Packet Inter Net Groper, allows a user to test basic connectivity.
The ping utility is a diagnostic tool you can use to test TCP/IP configurations and diagnose connection failures. Use the ping utility to determine whether a particular TCP/IP host is available and functional. To test connectivity, use the ping command with the following syntax:
ping <IP_address>

## Slide 8
Outline
Ping Command (Continue…)
A successful ping:
PC>ping 10.0.0.1
Pinging 10.0.0.1 with 32 bytes of data:
Reply from 10.0.0.1: bytes=32 time=49ms TTL=128
Reply from 10.0.0.1: bytes=32 time=7ms TTL=128
Reply from 10.0.0.1: bytes=32 time=7ms TTL=128
Reply from 10.0.0.1: bytes=32 time=8ms TTL=128
Ping statistics for 10.0.0.1:
Packets: Sent = 4, Received = 4, Lost = 0 (0% loss),
Approximate round trip times in milli-seconds:
Minimum = 7ms, Maximum = 49ms, Average = 17ms

## Slide 9
Outline
Ping Command (Continue…)
A failed ping:
PC>ping 10.0.0.3
Pinging 10.0.0.3 with 32 bytes of data:
Request timed out.
Request timed out.
Request timed out.
Request timed out.
Ping statistics for 10.0.0.3:
Packets: Sent = 4, Received = 0, Lost = 4 (100% loss)

## Slide 10
Outline
Ping Command (Continue…)

## Slide 11
Outline
Ping Command (Continue…)
ping [-t] [-a] [-n count] [-l length] <IP_address>
Parameters
    -t : Pings the specified computer until interrupted.
    -a : Resolves addresses to computer names.
    -n count : Sends the number of ECHO packets specified by count. The default is 4.
    -l length : Sends ECHO packets containing the amount of data specified by length. The default is 32 bytes; the maximum is 65,527.

## Slide 12
The following example illustrates how to send two pings, each 1450 bytes in size, to address 10.99.99.2:
C:\>ping -n 2 -l 1450 10.99.99.2
Pinging 10.99.99.2 with 1450 bytes of data:
Reply from 10.99.99.2: bytes=1450 time<10ms TTL=32
Reply from 10.99.99.2: bytes=1450 time<10ms TTL=32
Ping statistics for 10.99.99.2:
Packets: Sent = 2, Received = 2, Lost = 0 (0% loss),
Approximate round trip times in milliseconds:
Minimum = 0ms, Maximum = 0ms, Average = 0ms
Outline
Ping Command

## Slide 13
Outline
Ping Command
The following real example illustrates how to send a two pings command to IP 127.0.0.1

## Slide 14
The goal behind the trace route command is to help you troubleshoot and determine the path a packet is taking to get to a destination device. The syntax of trace route in host is:
tracert ip-address
Outline
Trace Route Command

## Slide 15
The following example illustrate tracert command
Outline
Trace Route Command
The following example illustrates the trace route command

## Slide 16
Outline
The Difference between Ping and Tracert
Ping
Tracert

## Slide 17
THANK YOU